## Slide 1
Full Pin List (by port)
PA | Function
PA0 | Gyro SCL (bit-bang I2C)
PA1 | Gyro SDA (bit-bang I2C)
PA7 | F_L motor IN1
PA8 | Color sensor LEFT
PA9 | Color sensor RIGHT
PA10 | UART0 TX -> Zigbee
PA11 | UART0 RX <- Zigbee
PA12 | F_L motor IN2
PA13 | F_R motor IN1
PA14 | B_L motor IN2
PA15 | F_L motor PWM TIMA0_CH2
PA16 | F_R motor IN2
PA21 | UART2 TX -> MaixCAM2
PA23 | B_R motor PWM TIMA0_CH3
PA24 | UART2 RX <- MaixCAM2
PA25 | Encoder L_B
PA26 | Encoder R_B
PA28 | OLED I2C0 SDA
PA31 | OLED I2C0 SCL
PB | Function
PB7 | Grayscale sensor CLK
PB8 | Grayscale sensor DAT
PB9 | B_L motor PWM TIMA0_CH1
PB13 | B_R motor IN1
PB14 | F_R motor PWM TIMA0_CH0
PB15 | B_R motor IN2
PB16 | B_L motor IN1
PB17 | KEY1 button
PB18 | KEY2 button
PB19 | KEY3 button
PB24 | Encoder L_A
PB25 | Encoder R_A
PA:20 . PB:12 . Total:32 (28 assigned)

## Slide 2
Communication Interfaces
Interface | TX | RX | Usage | Baud | Protocol
UART0 | PA10 | PA11 | Zigbee remote/status | 9600 | text frames
UART2 | PA21 | PA24 | MaixCAM2 ball detect | 115200 | 0xAA 0x55 9-byte
I2C0 | PA31(SCL) | PA28(SDA) | OLED 0.96in 4-line | 400k | HW I2C
GPIO I2C | PA0(SCL) | PA1(SDA) | JY61P gyro | ~100k | bit-bang I2C
Zigbee Data Format
Heartbeat: HB T:<tx> R:<rx> E:<echo> (every 1s) Echo mode: receive any byte -> send back unchanged Old protocol: Z<tx> S<state> D<dist> Y<yaw>
Resources: 28 GPIO . TIMA0 4/4ch . I2C0 1/1 . UART0+UART2 2/4 . SW I2C 1

## Slide 3
Sensors & Encoders
Encoders
Signal | Pin | Note
L_A | PB24 | 
L_B | PA25 | MM_PER_COUNT
R_A | PB25 | = 10.53 mm
R_B | PA26 | simple counting
Sensors
Sensor | Pin | Description
Gray CLK | PB7 | 8ch grayscale serial
Gray DAT | PB8 | 1=white line, 0=black
Color LEFT | PA8 | left trigger
Color RIGHT | PA9 | -> stop+back+turn seq
Gyro SCL | PA0 | JY61P bit-bang I2C
Gyro SDA | PA1 | 6-axis, addr 0x50
Buttons
Key | Pin
KEY1 | PB17
KEY2 | PB18
KEY3 | PB19

## Slide 4
Motor Driver - TB6612 (4ch PWM, TIMA0)
Motor | PWM Ch | IN1 | IN2 | Direction (forward)
F_L FrontL | PA15 CH2 | PA7 | PA12 | Swapped: IN1=0,IN2=1
F_R FrontR | PB14 CH0 | PA13 | PA16 | Normal: IN1=1,IN2=0
B_L BackL | PB9 CH1 | PB16 | PA14 | Normal: IN1=1,IN2=0
B_R BackR | PA23 CH3 | PB13 | PB15 | Normal: IN1=1,IN2=0
API: motor_control(left, right) range -1000 ~ +1000
Left side=F_L+B_L same speed | Right side=F_R+B_R same speed (skid steer)
F_L FRONT F_R L <-- --> R
B_L REAR B_R L <-- --> R

## Slide 5
MSPM0G3507 Pin Map
Amy 64pin 4-Wheel Line-Following Robot
UART0=Zigbee . UART2=MaixCAM2 . I2C0=OLED . TIMA0=4ch PWM
Electronics-Design | 2025-07